## Slide 1: Prototype Cylindrical µRwell Update
Jerry L. Collins II
2/21/2020

## Slide 2: Overview
3D Printed Frame printed by Brookhaven National Lab
Two Sides designed to be (approx.) equal size

## Slide 3: Frame A (Well Fitting Set)- Outer Ring
203mm (expected 203.891mm)
192.688mm (calc.)
193.891 (exp.)
5.156mm
5(exp.)
12.014mm
12 (exp.)

## Slide 4: Frame A- Middle Ring
191mm (193.789 exp.)
158.64mm (calc.)
161.789 (exp.)
11.976mm
12 (exp.)
16.18mm
16 (exp.)

## Slide 5: Frame A- Inner Ring
159mm (161.281 exp.)
151.054mm 151.281(exp.)
5.207mm
5 (exp.)
72.111mm
72 (exp.)

## Slide 6: Frame B (Less Well Fitting)- Outer Ring
202.5mm (203.638 expected)
192.34mm (calc.)
193.638mm expected
11.963mm
(12 exp.)
5.08mm (5 exp.)

## Slide 7: Frame B- Middle Ring
193.5mm (193.536 exp.)
160.836mm (calc.)
161.536 (exp.)
11.989mm
12 (exp.)
16.332mm
16 (exp.)

## Slide 8: Frame B- Inner Ring
160.5mm (161.028 exp.)
151.054mm (151.028 exp.)
72.022mm
72 (exp.)
5.004mm
5(exp.)

## Slide 9: Data Table
Frame | Part | Feature | Theoretical (mm) | Measured (mm) | Deviation | Percent Difference | Notes
A | Outer Ring | Height | 12 | 12.014 | 0.014 | 0.117 | positive dev. means larger than theor.
A | Outer Ring | Thickness | 5 | 5.156 | 0.156 | 3.120 | 
A | Outer Ring | Outer Diameter | 203.891 | 203 | -0.891 | -0.437 | 
A | Outer Ring | Inner Diameter | 193.891 | 192.688 | -1.203 | -0.620 | 
A | Middle Ring | Height | 12 | 11.976 | -0.024 | -0.200 | 
A | Middle Ring | Thickness | 16 | 16.18 | 0.18 | 1.125 | 
A | Middle Ring | Outer Diameter | 193.789 | 191 | -2.789 | -1.439 | 
A | Middle Ring | Inner Diameter | 161.789 | 158.64 | -3.149 | -1.946 | 
A | Inner Ring | Height | 72 | 72.111 | 0.111 | 0.154 | 
A | Inner Ring | Thickness | 5 | 5.207 | 0.207 | 4.140 | 
A | Inner Ring | Outer Diameter | 161.281 | 159 | -2.281 | -1.414 | 
A | Inner Ring | Inner Diameter | 151.281 | 151.054 | -0.227 | -0.150 | 
B | Outer Ring | Height | 12 | 11.963 | -0.037 | -0.308 | 
B | Outer Ring | Thickness | 5 | 5.08 | 0.08 | 1.600 | 
B | Outer Ring | Outer Diameter | 203.638 | 202.5 | -1.138 | -0.559 | 
B | Outer Ring | Inner Diameter | 193.638 | 192.34 | -1.298 | -0.670 | 
B | Middle Ring | Height | 12 | 11.989 | -0.011 | -0.092 | 
B | Middle Ring | Thickness | 16 | 16.332 | 0.332 | 2.075 | 
B | Middle Ring | Outer Diameter | 193.536 | 193.5 | -0.036 | -0.019 | 
B | Middle Ring | Inner Diameter | 161.536 | 160.836 | -0.7 | -0.433 | 
B | Inner Ring | Height | 72 | 72.022 | 0.022 | 0.031 | 
B | Inner Ring | Thickness | 5 | 5.004 | 0.004 | 0.080 | 
B | Inner Ring | Outer Diameter | 161.028 | 160.5 | -0.528 | -0.328 | 
B | Inner Ring | Inner Diameter | 151.028 | 151.054 | 0.026 | 0.017 |